## Slide 1
Implementation of AES in FPGA Hardware
Presenters:
Najmeh Nazari
August 2020
1

## Slide 2
Outline
Goal
Overview on Advanced Encryption Standard (AES)
Review of RTL Design Methodology
Hardware Implementation of AES
2

## Slide 3: Goal
Develop the RTL code of AES.
Based on the RTL design
  Design the Datapath
  Design the controller unit for their hardware
Perform the implementation of the design

## Slide 4: Overview on AES (I)
AES is a popular cipher: a method or process used to change raw information. (Encryption)
  uses a known, external piece of information (key), to uniquely change the data.
Reversible: it can be applied again to put the information back into its original form (Decryption)
AES includes three block ciphers :
AES-128: Confidential
AES-192: Secret
AES-256: Top Secret
Block Size :128 bit = 16 byte
Each cipher encrypts and decrypts data in blocks of 128 bits
The most secure
Fastest

## Slide 5: Overview on AES (II)
XOR
Byte Sub
ShiftRows
MixColumns
Add round key
Substitution
Permutation

## Slide 6: RTL Design Methodology
Structure of a Typical Digital System

## Slide 7: Hardware Design with RTL VHDL

## Slide 8: Steps of the Design Process
1. Text description
2. Interface
3. Pseudocode
4. Block diagram of the Datapath
5. Interface divided into the Datapath and Controller
6. ASM chart of the Controller
7. RTL VHDL code of the Datapath, Controller, and Top-Level Unit
8. Testbench for the Datapath, Controller, and Top-Level Unit
9. Functional simulation and debugging
10. Synthesis and post-synthesis simulation
11. Implementation and timing simulation
12. Experimental testing using FPGA board

## Slide 9: Exercise : Pseudocode
Calculates the average of K numbers and keep the 3 largest values in no_1, no_2, and no_3

## Slide 10: Exercise : Circuit Interface
Based on the Pseudocode, determine what functions input and output your design needs (clock, reset, inputs, outputs, control signals, state signals)

## Slide 11: Exercise : Interface Table
Define the specification of your design clearly

## Slide 12: Exercise : Block diagram of the Datapath
Based on the Pseudocode, decide what functions you need in your data path (counter, comparator, shifter, multiplier, adder, … )
Determine the control and status signals that you need to control the functionality of datapath

## Slide 13: Exercise : Interface with the division into the Datapath and Controller
Connect datapath to controller

## Slide 14: Timing Analysis- Critical Path

## Slide 15: Setup & Hold Time of a Register

## Slide 16: Elements used in ASM charts

## Slide 17: ASM Block

## Slide 18: ASM Chart Rules
Difference between a regular flowchart and an ASM chart:
  Transition governed by clock
  Transition occurs between ASM blocks
Basic rules:
  For a given input combination, there is one unique exit path from the current ASM block
  Any closed loop in an ASM chart must include a state box

## Slide 19: Example : State Diagram

## Slide 20: Example : ASM Chart

## Slide 21: Exercise: Control Unit

## Slide 22: AES
Check the Pseudocode
Design Datapath
Design Control Unit

## Slide 23: AES Encryption Pseudocode

## Slide 24: Symbol

## Slide 25: AES_Enc: Interface with the Division into the Datapath and Controller
Note: Bold line represents a 128-bit bus unless specified otherwise

## Slide 26: AES Datapath
Note: Bold line represents a 128-bit bus unless specified otherwise

## Slide 27: Round Block Diagram
Note: Bold line represents a 128-bit bus unless specified otherwise

## Slide 28: KeyUpdate Block Diagram
Note: All buses are 32-bit wide unless specified otherwise

## Slide 29: Control Unit
Bold line represents a 128-bit bus unless specified otherwise

## Slide 30: Thank you